    Fitting with replaceable
    resistance thermometer inset
Screw-in
resistance thermometer
Form 2G in accordance with DIN 43735 / 43772
Krick Meßtechnik & Partner GmbH & Co. KG Sparkasse Oberhessen	Telefon 06184/92390 Geschäftsführer
Am Bahnhof 6a	Filiale Echzell	Telefax /923922 Dipl.-Ing. Herbert Krick
D-63505 Langenselbold	BIC : Hela de F1 FRI	E-Mail info@kmp-online.de Amtsgericht Hanau HRA 5106
USt.Id-Nr.: DE 811534429	IBAN: DE 5751850079 0085 002 279	Pers. Haftender Gesellschafter: KMP Verwaltungs-GmbH, Amtsgericht Hanau HRB 95891
Krick Meßtechnik & Partner GmbH & Co. KG Sparkasse Oberhessen	Telefon 06184/92390 Geschäftsführer
Am Bahnhof 6a	Filiale Echzell	Telefax /923922 Dipl.-Ing. Herbert Krick
D-63505 Langenselbold	BIC : Hela de F1 FRI	E-Mail info@kmp-online.de Amtsgericht Hanau HRA 5106
USt.Id-Nr.: DE 811534429	IBAN: DE 5751850079 0085 002 279	Pers. Haftender Gesellschafter: KMP Verwaltungs-GmbH, Amtsgericht Hanau HRB 95891

    Fitting with replaceable
    resistance thermometer inset
Screw-in resistance thermometer
Form 2G according to DIN 43735 / 43772
Structure of the fitting:
Structure Form 2G according to DIN 43772 with	protective tube diameter of 9 – 14 mm and screw neck	G1“ or G½“ and extension pipe. Connection head made	of light metal Form A or Form B according to DIN 50446
with cable entry M20x1.5.
(For variants please refer to the worksheet).

Structure of the inset in accordance
with DIN 43735:
Precision resistor single or dual, Type Pt-100
        Basic values as per IEC 60751 in Tolerance class B or A.
Connected in 2-, 3- or 4-wire circuit from
precision resistor, installed in a rigid inset pipe of	stainless steel material or as sheath resistance	thermometer inset in flexible version with a diameter of	6 mm.
Shelf plate with connection socket.

(For variants please refer to the worksheet).

Design of resistance thermometer:
Temperatures up to 600°C standard, on request with Nickel-feed lines and Inconel inset pipe for temperatures up to 800°C; Additional type specification “HT”. Precision resistor is insulated in a ceramic powder and vibrated and sealed airtight.
In flexible version up to 450°C as standard, over that with mineral insulated sheath cable of Inconel material and internal nickel leads for temperatures up to 800°C; Additional type specification “HT”. Precision resistor is
insulated in a ceramic powder and vibrated and sealed airtight.
Even shockproof and high vibration resistant versions are available; additional type specification “E”.
For pressure resistant and stable flow versions, also refer to the section Special versions or ask our technical customer service.

Types of wiring:	Areas of application:

Plant, pipeline and tank construction
Heating and air conditioning technology
Power plant technology
Furnace construction
Chemicals
for gas, steam, fluids and granulates
     Pt-100 2-lead	Pt-100 3-lead Pt-100 4-lead

Protective tube diameter D:	Protective tube material:
 6 x 1.0mm	|☺|	1.4541 (V2A)	|☺|
 9 x 1.0mm	|☺|	1.4571 (V4A)	|☺|
11 x 1.0mm	|☺|	others	|☺|
11 x 2.0mm	|☺|
14 x 2.5mm	|☺|
others	|☺|

Screw neck:	Neck material:
G ½“	|☺|	1.4541 (V2A)	|☺|
G 1“	|☺|	1.4571 (V4A)	|☺|
others	|☺|	others	|☺|

Protective tube length NL:	Extension pipe length HL:
160mm	|☺|	145mm	|☺|
250mm	|☺|	others ______	|☺|
400mm	|☺|
others	______	|☺|

Connector head:
Form A	Light metal |☺|
Form B	Light metal |☺|
Others

Temperature load: Measurement point: from| | to | | °C Environment/Connector head: | | °C
_____________________________________________________________________________ ______________

Calculation of the inset length = Protective tube length + Extension pipe length + 10mm
__________________________________________________________________________________ _________

Sheath resistance thermometer inset:	Additional specification/ Remarks:
Pt-100	single |☺|	dual	|☺|

Pt-1000	single |☺|	dual	|☺|
Others | |
2-|☺|	3-|☺|	4-|☺| wire circuit

Tolerance class
Class B |☺|
Class A |☺|
Others | |

Company	:| |	Your Ref.	:| |
Contact person	:| |	Quantity	:| |
Street/Place	:| |	Del. time	:| |
Email address	:| |	Telephone	:| |